## Slide 1
Sequential Logic Circuits
Intelligent Traffic Signal Decision System
Group 9
_______________
1

## Slide 2
The Big Idea: Sequential Logic
Connecting the intelligent traffic signal to the CPU memory-and-stepping concept
• Combinational logic produces outputs from present inputs only.
• Sequential logic adds memory: the controller can remember the current signal state.
• A clock lets the system change traffic phases in an organized, repeatable way.
• The controller remembers whether the junction is RED, GREEN, YELLOW, or in EMERGENCY mode.
• This same memory-and-stepping idea is used by CPUs to control sequences of operations.
2

## Slide 3
Why Does the Traffic Signal Need Memory?
Traffic sensors
Sequential Controllers
Traffics llights
• If the road has a green phase, vehicles are allowed to move.
• The signal must remain green for a controlled interval before changing.
• The controller must pass through YELLOW before RED for safe switching.
• An emergency vehicle can request priority, so the controller needs stored state and controlled transitions.
3

## Slide 4
System Specification
Input / Element | Meaning
D | Traffic-density sensor
P | Pedestrian-request sensor
E | Emergency-priority sensor
CLK | Phase/timing clock
RESET | Initializes controller
SIGNALS | RED / YELLOW / GREEN outputs
Goal
Adaptive signal control
Safety
Controlled phase changes
Memory
Store signal state
4

## Slide 5
Latches and Flip-Flops
SR Latch
Basic memory element
D Latch
Level-sensitive
D Flip-Flop
Edge-triggered
• SR latch stores a bit using feedback.
• D latch follows the input while enabled and holds it when disabled.
• D flip-flop captures the next-state value at a clock edge and holds it.
• For the traffic signal, D flip-flops are convenient for storing the FSM state.
5

## Slide 6
Clock and Synchronous Design
Traffic Inputs
Next-State Logic
D Flip-Flops
CLOCK
• All state elements update on a chosen clock edge.
• Clocking makes signal timing easier to design and simulate.
• Setup time: inputs should be stable before the active edge.
• Hold time: inputs should remain stable briefly after the active edge.
• A timing signal can represent the end of a green/yellow phase.
6

## Slide 7
Registers: Storing Multi-Bit Signal State
DFF 1
DFF 2
DFF 3
DFF 4
A row of flip-flops forms a register
• In a CPU, registers store operands, addresses, and intermediate values.
• In our project, the state register stores the current traffic-signal state.
• Each flip-flop stores one bit of the state.
• Two bits can encode four states: RED, GREEN, YELLOW and EMERGENCY.
7

## Slide 8
Shift Registers — Brief Connection
1
0
1
1
Shift registers move stored bits left or right on clock edges.
• Shift registers are useful in serial communication, data transfer, delay lines and temporary storage.
• The traffic signal mainly needs state storage, so a simple state register/FSM is sufficient.
• A shift register can be added later for serial sensor data or communication with a traffic-control unit.

## Slide 9
Counters and the Program-Counter Pattern
Clock
Synchronous Counter
Time / Phase Count
Clock | Counter
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
• A synchronous counter changes its stored value on clock edges.
• A CPU's program counter stores which instruction is next.
• The traffic controller can use a counter to measure the duration of RED, GREEN and YELLOW phases.
• When the required count is reached, the FSM moves to the next signal state.
9

## Slide 10
Finite State Machine (FSM)
Present State
Next-State Logic
Next State
CLOCK
• An FSM describes step-by-step traffic-signal behavior using states and transitions.
• State transitions depend on the current state, timer condition and sensor inputs.
• The FSM is the control unit of the digital traffic signal system.
• Emergency input can override normal sequencing and move the controller to a priority state.
10

## Slide 11
Intelligent Traffic Signal FSM — State Diagram
S0
RED
All stop
S1
GREEN
Traffic ON
S2
YELLOW
Transition
Timer / sensor condition
S3 EMERGENCY
Priority mode
Normal sequence: RED → GREEN → YELLOW → RED
Emergency detected → S3; emergency cleared → return to safe RED state
11

## Slide 12
FSM State Table
Present State | Input / Condition | Next State | Output
S0 RED | Normal + timer | S1 GREEN | RED ON
S1 GREEN | Timer complete | S2 YELLOW | GREEN ON
S2 YELLOW | Timer complete | S0 RED | YELLOW ON
Any state | E = 1 | S3 EMERGENCY | Priority mode
S3 EMERGENCY | E = 0 | S0 RED | Protected RED
• The exact sensor encoding can be adapted to the simulator used.
• A practical design can add hysteresis so the pump does not chatter around a boundary.
12

## Slide 13
State Encoding with D Flip-Flops
State | Q1 | Q0 | Pump
LOW | 0 | 0 | ON
MEDIUM | 0 | 1 | ON
FULL | 1 | 0 | OFF
Unused | 1 | 1 | —
Two D flip-flops
store Q1 and Q0
D inputs = next-state
values
Clock edge updates
Q1 Q0
13

## Slide 14
Traffic Signal Control Logic
RED
00 → ON
GREEN
01 → ON
YELLOW
10 → ON
RED = Q1′Q0′ + Q1Q0
GREEN = Q1′Q0
YELLOW = Q1Q0′
• The stored state determines which signal output is active.
• State 00 produces RED, 01 produces GREEN and 10 produces YELLOW.
• State 11 represents EMERGENCY priority; it can force a protected red condition for conflicting traffic.
• Real signal outputs should use suitable LED drivers/relays and electrical isolation.
14

## Slide 15
Simulation Design
Sensors
D / P / E
Next-State
Logic
D Flip-Flops
Q1 Q0
Traffic LEDs /
Driver
CLOCK
• Use switches to simulate traffic-density (D), pedestrian request (P) and emergency (E) inputs.
• Use LEDs to display RED, YELLOW, GREEN and emergency state.
• Apply RESET first, then change sensor conditions and observe transitions at clock edges.
• Verify every state against the FSM table.
15

## Slide 16
Simulation Sequence / Expected Output
Clock | Traffic Condition | State | Signal Output
0 | Initial / RESET | S0 RED | RED
1 | Normal traffic | S1 GREEN | GREEN
2 | Green timer complete | S2 YELLOW | YELLOW
3 | Yellow timer complete | S0 RED | RED
4 | Emergency detected | S3 EMERGENCY | Priority RED
5 | Emergency cleared | S0 RED | RED
6 | High density | S1 GREEN | GREEN
7 | Phase complete | S2 YELLOW | YELLOW
16

## Slide 17
Milestone: Working Sequential-Logic Fabric
1. Working Register
Stores signal state
2. Counter Pattern
Times each phase
3. Working FSM
Controls signals
• Register → remembers the current traffic-signal state.
• Clock/counter pattern → provides controlled phase timing.
• FSM → converts sensor conditions into safe state transitions.
• Together these form the memory-and-stepping fabric behind the intelligent traffic controller.
Sensors → FSM → Flip-Flops → Signal Lights
Sensors → FSM → Flip-Flops → Pump
17

## Slide 18
Advantages, Applications & Limitations
Advantages
• Automatic signal sequencing
• Better response to changing traffic conditions
• Emergency priority can be included
• Reduced manual monitoring
• Easy digital simulation and verification
Applications
• Smart city intersections
• Busy junctions and highways
• School and hospital zones
• Emergency vehicle priority systems
• Traffic-management prototypes
Limitations
• Sensor faults can affect decisions
• Clock/timer design affects response
• Driver and electrical isolation are required
• Poor sensor placement affects accuracy
• Real intersections need additional safety and coordination logic
18

## Slide 19
Conclusion
Intelligent Traffic Signal = Sensors + Memory + Clock + FSM + Signal Control
• Sequential logic allows the controller to remember its current traffic-signal state.
• D flip-flops store the state, while combinational logic determines the next state.
• Counters/timing provide controlled signal durations.
• The FSM coordinates RED, GREEN, YELLOW and emergency-priority transitions.
• Simulation and truth/state tables verify that the designed outputs follow the required logic.
• The system can be extended with more lanes, IoT monitoring, camera detection and adaptive timing.
Sense → Remember → Decide → Control
19

## Slide 20
THANK YOU
Questions?
Intelligent Traffic Signal Decision System
20