## Slide 1
INTELLIGENT TRAFFIC SIGNAL
DECISION SYSTEM
Design and simulation using combinational logic
Digital Design & Computer Architecture (DDCA)
Logisim / digital-logic simulation project

## Slide 2
2. Problem Statement
Why intelligent traffic control?
• Fixed-time traffic signals may not respond to changing traffic conditions.
• Uneven vehicle density can cause unnecessary waiting and congestion.
• Emergency vehicles may require immediate priority.
• A digital decision system can process sensor inputs and select the required signal state automatically.
Project idea
• Use binary inputs from traffic sensors.
• Apply Boolean logic and combinational circuits.
• Generate red, yellow and green control outputs.
• Verify the design using a truth table and simulation.

## Slide 3
3. Objectives
Design
• Develop a combinational traffic decision system.
• Represent traffic conditions using binary inputs.
• Create simplified Boolean expressions.
Implement
• Use NOT, AND and OR gates.
• Build the logic in Logisim.
• Generate mutually controlled traffic outputs.
Verify
• Prepare the truth table.
• Test normal, congested and emergency cases.
• Compare simulated outputs with expected results.

## Slide 4
4. System Overview
Traffic Sensors
D, P, E
Logic Unit
AND / OR / NOT
Decision Controller
Priority logic
Traffic Signals
R / Y / G
Inputs are evaluated continuously; the combinational logic determines which traffic indication should be active.

## Slide 5
5. Input Variables / Sensors
D — Traffic Density
0 = low/normal density
1 = high density
Represents whether the monitored approach has significant traffic.
P — Pedestrian Request
0 = no crossing request
1 = pedestrian crossing request
Used to trigger a controlled transition for pedestrians.
E — Emergency Priority
0 = normal operation
1 = emergency vehicle detected
Emergency input receives highest decision priority.

## Slide 6
6. Decision Rules
Priority logic
• If E = 1, the system enters emergency-priority mode.
• If E = 0 and P = 1, the system provides a safe pedestrian transition.
• If E = 0 and P = 0, traffic density D controls normal signal timing.
• The logic is combinational: outputs depend on the present input combination.
Normal-mode interpretation
D = 0 → normal/low traffic condition
D = 1 → high traffic condition
The controller can allocate the green phase to the selected approach when density is high, while maintaining yellow and red safety states during transitions.

## Slide 7
7. Truth Table
E | P | D | R | Y | G
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0
E = emergency, P = pedestrian request, D = high density. R/Y/G are red, yellow and green control outputs.

## Slide 8
8. Boolean Expressions
Red output (R)
R = E + P·D̅
Yellow output (Y)
Y = E̅·P
Green output (G)
G = E̅·P̅·D
Meaning
• NOT gates generate complemented inputs such as E̅ and P̅.
• AND gates form conditions; OR combines alternative conditions.
• The expressions can be simplified further using Boolean algebra or K-Maps.

## Slide 9
9. K-Map / Simplification
Example: Green output
For G = 1, the required condition is:
E = 0, P = 0, D = 1
Therefore:
G = E̅ · P̅ · D
The K-Map confirms the minterm corresponding to this operating condition.
Why simplify?
• Fewer gates can reduce circuit complexity.
• Shorter expressions are easier to implement in Logisim.
• Simplification improves readability and verification.
• Each output can be tested independently against the truth table.

## Slide 10
10. Logic Gates Used
NOT
Inverts an input
NOT
AND
All required inputs must be 1
AND
OR
Any active condition can produce 1
OR

## Slide 11
11. System Architecture
Traffic Sensors
Density D
Pedestrian P
Emergency E
Logic Unit
NOT gates
AND / OR gates
Boolean expressions
Decision Controller
Priority logic
Signal-state selection
Outputs
Red R
Yellow Y
Green G
The modular structure makes the design easier to test, simulate and extend.

## Slide 12
12. Hardware / Simulation Components
Traffic Sensors
• Vehicle-density sensor
• Pedestrian request sensor
• Emergency-vehicle detector
• Provide binary signals to the logic circuit.
Logic / Controller
• Digital logic gates
• Combinational decision circuit
• Logisim implementation
• Processes the current sensor inputs.
Signal Outputs
• Red LED / signal
• Yellow LED / signal
• Green LED / signal
• Can be connected to a physical controller in an extended prototype.

## Slide 13
13. Control Algorithm
1. START
Initialize inputs and outputs.
2. READ
Read E, P and D.
3. CHECK
Evaluate emergency priority first.
4. DECIDE
Apply Boolean expressions.
5. ACT
Update R, Y and G.
6. REPEAT
Continue monitoring the inputs.

## Slide 14
14. Simulation Scenarios
Case 1 — Normal
• E = 0, P = 0, D = 0
• Normal traffic condition.
• Red/green selection follows the designed normal-mode logic.
Case 2 — High Density
• E = 0, P = 0, D = 1
• High vehicle density is detected.
• Green output becomes active for the selected approach.
Case 3 — Emergency
• E = 1
• Emergency priority overrides normal traffic conditions.
• Red is asserted for the protected conflicting movement.

## Slide 15
15. Expected Simulation Results
Scenario | E | P | D | Expected output
Normal / low traffic | 0 | 0 | 0 | R=1, Y=0, G=0
High traffic | 0 | 0 | 1 | R=0, Y=0, G=1
Pedestrian request | 0 | 1 | 0 | R=0, Y=1, G=0
Pedestrian + high density | 0 | 1 | 1 | R=0, Y=1, G=0
Emergency priority | 1 | X | X | R=1, Y=0, G=0
X = don't-care input in emergency-priority mode. Verify every row in Logisim.

## Slide 16
16. Applications, Advantages & Future Scope
Applications
• Smart city intersections
• Busy junctions and highways
• School / hospital zones
• Emergency vehicle priority systems
• Adaptive traffic-management prototypes
Advantages
• Fast digital decision making
• Simple combinational implementation
• Easy simulation and verification
• Reduces dependence on fixed conditions
• Can be expanded with additional sensors
Future Scope
• Multiple-road adaptive control
• IoT traffic monitoring
• Camera-based vehicle detection
• Mobile / control-room alerts
• Fault detection and event logging
• AI-assisted traffic prediction

## Slide 17
17. DDCA Concepts Demonstrated
Core concepts
• Binary representation of sensor states
• Boolean algebra and Boolean expressions
• Truth tables and K-Maps
• NOT, AND and OR gates
• Combinational logic design
• Simulation and verification in Logisim
Extension to digital design
• MUX / decoder concepts can be added for multi-road selection.
• Comparators can be used for traffic-count thresholds.
• Sequential logic can store timing or phase information.
• ALU concepts connect the project to broader digital computer architecture topics.

## Slide 18
18. Conclusion
The Intelligent Traffic Signal Decision System applies combinational logic to traffic-management decisions.
It converts sensor conditions into binary inputs and processes them using Boolean expressions and logic gates.
Truth tables and K-Maps provide a systematic method to design and simplify the circuit.
The Logisim simulation can be used to verify that the outputs match the expected traffic conditions.
The design can be extended with more lanes, sensors, IoT monitoring, camera inputs, adaptive timing and fault detection.
Project takeaway
Sense → Process with combinational logic → Decide → Control traffic signals